Lab 3: Configuring VTP Clients and Servers on Catalyst Switches

Lab Objective:
The objective of this lab exercise is for you to learn and understand how to configure VTP Server and Client mode on Cisco Catalyst switches. By default, all Cisco switches are VTP Server devices.
Lab Purpose:
VTP Client and Server mode configuration is a fundamental skill. VLANs are configured on VTP Servers and VTP Clients receive VLAN information from the VTP Servers in the same VTP domain. VLAN sharing is possible by using a trunk between the switches. As a Cisco engineer, as well as in the Cisco CCNA exam, you will be expected to know how to configure VTP Client and Server mode.
Certification Level:
This lab is suitable for both CCENT and CCNA certification exam preparation
Lab Difficulty:
This lab has a difficulty rating of 5/10
Readiness Assessment:
When you are ready for your certification exam, you should complete this lab in no more than 15 minutes
Lab Topology:
Please use the following topology to complete this lab exercise:

Task 1:
In preparation for VLAN configuration, configure a hostname on Sw1 as well as the VLANs depicted in the topology. Keep in mind that the default mode of operation of Cisco Catalyst switches is VTP Server mode.
Task 2:
Configure and verify Sw1 as a VTP Server switch and configure Sw2 as a VTP Client switch. Both switches should be in the VTP domain named CISCO.
Task 3:
Configure and verify FastEthernet0/1 between Sw1 and Sw2 as an 802.1q trunk
Task 4:
Configure and verify VLANs 10 and 20 on Sw1 with the names provided above. Assign FastEthernet0/2 on both Sw1 and Sw2 to VLAN 10. This interface should be configured as an access port.
Task 5:
Configure R1 and R3 FastEthernet0/0 interfaces with the IP addresses 10.0.0.1/28 and 10.0.0.3/28 respectively. Test connectivity via your VLANs by pinging R1 from R3 and vice versa.

SOLUTION:
Lab 3 Configuration and Verification
Task 1:
Switch#config t
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#hostname Sw1
Sw1(config)#
Switch#config t
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#hostname Sw2
Sw1(config)#
Router#config t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#hostname R1
R1(config)#
Router#config t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#hostname R3
R3(config)#

Task 2:
NOTE: By default, Cisco switches are VTP servers so no configuration is necessary for Server mode on Sw1. This can be verified using the show vtp status command. However, we do need to configure the domain.

Sw1#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw1(config)#vtp domain CISCO
Changing VTP domain name from Null to CISCO
Sw1(config)#
Sw2#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw2(config)#vtp mode client
Setting device to VTP CLIENT mode.
Sw2(config)#vtp domain CISCO
Changing VTP domain name from Null to CISCO
Sw2(config)#end
Sw1#show vtp status VTP Version	: 2
Configuration Revision	: 7
Maximum VLANs supported locally	: 250
Number of existing VLANs	: 7
VTP Operating Mode	: Client
VTP Domain Name	: CISCO
VTP Pruning Mode	: Enabled
VTP V2 Mode	: Disabled
VTP Traps Generation	: Disabled
MD5 digest	: 0x9D 0x1A 0x9D 0x16 0x9E 0xD1 0x38 0x59

Task 3:

NOTE: By default Cisco switches default to 802.1q trunking so no explicit configuration is required.
Sw1#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw1(config)#interface fastethernet0/1
Sw1(config-if)#switchport mode trunk
Sw1#show interfaces trunk
Port Mode Encapsulation Status Native vlan
Fa0/1 on 802.1q trunking 1
Port Vlans allowed on trunk
Fa0/1 1-4094
Port Vlans allowed and active in management domain
Fa0/1 1,10,20
Port Vlans in spanning tree forwarding state and not pruned
Fa0/1 1,20
Sw2#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw2(config)#interface fastethernet0/1
Sw2(config-if)#switchport mode trunk
Sw2#show interfaces trunk
Port Mode Encapsulation Status Native vlan
Fa0/1 on 802.1q trunking 1
Port Vlans allowed on trunk
Fa0/1 1-4094
Port Vlans allowed and active in management domain
Fa0/1 1,10,20
Port Vlans in spanning tree forwarding state and not pruned
Fa0/1 1,20
Task 4:
Sw1#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw1(config)#vlan 10
Sw1(config-vlan)#name SALES
Sw1(config-vlan)#exit
Sw1(config)#vlan 20
Sw1(config-vlan)#name MANAGERS
Sw1(config-vlan)#exit
Sw1(config)#interface fastethernet0/2
Sw1(config-if)#switchport mode access
Sw1(config-if)#switchport access vlan 10
Sw1(config-if)#end
Sw1#
Sw1#show vlan brief VLAN	Name		Status		Ports
----	--------------------------------		---------		-------------------------------
1	default		active		Fa0/1, Fa0/3, Fa0/4
Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gi0/1, Gi0/2
10	SALES		active		Fa0/2
20		MANAGERS		active
1002		fddi-default		active
1003		token-ring-default		active
1004		fddinet-default		active
1005		trnet-default		active

Sw2(config-if)#switchport mode access
Sw2(config-if)#switchport access vlan 10
Sw2(config-if)#end
Sw2#
Sw2#show vlan brief VLAN	Name		Status		Ports
----	--------------------------------		---------		-------------------------------
1	default		active		Fa0/1, Fa0/3, Fa0/4
Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gi0/1, Gi0/2
10	SALES		active		Fa0/2
20		MANAGERS		active
1002		fddi-default		active
1003		token-ring-default		active
1004		fddinet-default		active
1005		trnet-default		active

Task 5:
R1#config t
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)#interface fastethernet0/0
R1(config-if)#ip address 10.0.0.1 255.255.255.240
R1(config-if)#no shutdown
R1(config-if)#end
R1#
R3#config t
Enter configuration commands, one per line. End with CNTL/Z.
R3(config)#interface fastethernet0/0
R3(config-if)#ip address 10.0.0.3 255.255.255.240
R3(config-if)#no shutdown
R3(config-if)#end
R3#
R1#show ip interface brief
Interface IP-Address OK? Method Status Protocol
FastEthernet0/0 10.0.0.1 YES manual up up
R1#ping 10.0.0.3
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.0.0.3, timeout is 2 seconds:
.!!!!
Success rate is 80 percent (4/5), round-trip min/avg/max = 1/3/4 ms / NOTE: The first PING packet times out due to ARP resolution. Subsequent packets will be successful.

R3#show ip interface brief
Interface	IP-Address	OK?	Method	Status	Protocol
FastEthernet0/0	10.0.0.3	YES	manual	up	up
R3#ping 10.0.0.1
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.0.0.1, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 1/3/4 ms