Lab 4: Configuring VTP Transparent Mode

Lab Objective:
The objective of this lab exercise is for you to learn and understand how to configure VTP Transparent mode on Cisco Catalyst switches. By default, all Cisco switches are VTP Server devices.
Lab Purpose:
VTP Transparent mode configuration is a fundamental skill. VLANs configured on a switch in VTP Transparent mode are not automatically propagated to other switches within the same VTP domain as would be done by a VTP Server. Switches configured in VTP Transparent mode use a trunk to forward traffic for configured VLANs to other switches. As a Cisco engineer, as well as in the Cisco CCNA exam, you will be expected to know how to configure VTP Transparent mode.
Certification Level:
This lab is suitable for both CCENT and CCNA certification exam preparation
Lab Difficulty:
This lab has a difficulty rating of 5/10
Readiness Assessment:
When you are ready for your certification exam, you should complete this lab in no more than 15 minutes
Lab Topology:
Please use the following topology to complete this lab exercise:

Task 1:
In preparation for VLAN configuration, configure a hostname on switches 1 and 2 and routers 1 and 3 as illustrated in the topology.
Task 2:
Configure and verify Sw1 and Sw2 in VTP Transparent mode. Both switches should be in the VTP domain named CISCO. Remember that switches must be in the same VTP domain to share VLAN information via a trunk.
Task 3:
Configure and verify FastEthernet0/1 between Sw1 and Sw2 as an 802.1q trunk.
Task 4:
Configure and verify VLANs 2010 and 2030 on Sw1 with the names provided above. Assign FastEthernet0/2 on Sw1 to VLAN 2010 as an access port. Configure and verify VLANs 2010 and 2040 on Sw2 with the names provided above. Assign FastEthernet0/2 on Sw2 to VLAN 2010 as an access port.
Task 5:
Configure R1 and R3 FastEthernet interfaces with the IP addresses 10.0.0.1/28 and 10.0.0.3/28 respectively. Test VLAN connectivity by pinging between R1 and R3.
SOLUTION:
Lab 4 Configuration and Verification
Task 1:
Switch#config t
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#hostname Sw1
Sw1(config)#
Switch#config t
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#hostname Sw2
Sw1(config)#
Router#config t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#hostname R1
R1(config)#
Router#config t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#hostname R3
R3(config)#
Task 2:
Sw1#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw1(config)#vtp mode transparent
Setting device to VTP TRANSPARENT mode.
Sw1(config)#end
Sw1#show vtp status

VTP Version	: 2
Configuration Revision	: 2
Maximum VLANs supported locally	: 250
Number of existing VLANs	: 5
VTP Operating Mode	: Transparent
VTP Domain Name	: CISCO
VTP Pruning Mode	: Enabled
VTP V2 Mode	: Disabled
VTP Traps Generation	: Disabled
MD5 digest	: 0x9D 0x1A 0x9D 0x16 0x9E 0xD1 0x38 0x59
Configuration last modified by 10.1.1.3 at 3-1-93 01:42:39

Sw2#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw2(config)#vtp mode transparent
Setting device to VTP TRANSPARENT mode.
Sw2(config)#end
Sw2#show vtp status
VTP Version : 2
Configuration Revision : 2
Maximum VLANs supported locally : 250
Number of existing VLANs : 5
VTP Operating Mode : Transparent
VTP Domain Name : CISCO
VTP Pruning Mode : Enabled
VTP V2 Mode : Disabled
VTP Traps Generation : Disabled
MD5 digest : 0x9D 0x1A 0x9D 0x16 0x9E 0xD1 0x38 0x59
Configuration last modified by 10.1.1.3 at 3-1-93 01:42:45
Task 3: NOTE: By default Cisco switches default to 802.1q trunking so no explicit configuration is required.

Sw1#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw1(config)#interface fastethernet0/1
Sw1(config-if)#switchport mode trunk
Sw2#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw2(config)#interface fastethernet0/1
Sw2(config-if)#switchport mode trunk
Task 4:
Sw1#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw1(config)#vlan 2010
Sw1(config-vlan)#name SALES
Sw1(config-vlan)#exit
Sw1(config)#vlan 2030
Sw1(config-vlan)#name MANAGEMENT
Sw1(config-vlan)#exit
Sw1(config)#interface fastethernet0/2
Sw1(config-if)#switchport mode access
Sw1(config-if)#switchport access vlan 2010
Sw1(config-if)#end
Sw1#
Sw1#show vlan brief VLAN	Name		Status		Ports
----	--------------------------------		---------		-------------------------------
1	default		active		Fa0/1, Fa0/3, Fa0/4
Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gi0/1, Gi0/2
1002		fddi-default		active
1003		token-ring-default		active
1004		fddinet-default		active
1005		trnet-default		active
2010	SALES		active		Fa0/2
2030		MANAGEMENT		active

Sw2#config t
Enter configuration commands, one per line. End with CNTL/Z.
Sw2(config)#vlan 2010
Sw2(config-vlan)#name SALES
Sw2(config-vlan)#exit
Sw2(config)#vlan 2040
Sw2(config-vlan)#name DIRECTORS
Sw2(config-vlan)#exit
Sw2(config)#interface fastethernet0/2
Sw2(config-if)#switchport mode access
Sw2(config-if)#switchport access vlan 2010
Sw2(config-if)#end
Sw2#
Sw2#show vlan brief VLAN	Name		Status		Ports
----	--------------------------------		---------		-------------------------------
1	default		active		Fa0/1, Fa0/3, Fa0/4
Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gi0/1, Gi0/2
1002		fddi-default		active
1003		token-ring-default		active
1004		fddinet-default		active
1005		trnet-default		active
2010	SALES		active		Fa0/2
2040		DIRECTORS		active

NOTE: By default switches configured for VTP Transparent mode do not exchange VLAN information. You can see in the above output that VLAN 2030 on Sw1 is not propagated to Sw2, and VLAN 2040 on Sw2 is not propagated to Sw1. In Transparent mode, all VLANs must be manually configured on all switches.
Task 5:
R1#config t
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)#interface fastethernet0/0
R1(config-if)#ip address 10.0.0.1 255.255.255.240
R1(config-if)#no shutdown
R1(config-if)#end
R3#config t
Enter configuration commands, one per line. End with CNTL/Z.
R3(config)#interface fastethernet0/0
R3(config-if)#ip address 10.0.0.3 255.255.255.240
R3(config-if)#no shutdown
R3(config-if)#end
R1#show ip interface brief
Interface IP-Address OK? Method Status Protocol
FastEthernet0/0 10.0.0.1 YES manual up up
R1#ping 10.0.0.3
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.0.0.3, timeout is 2 seconds:
.!!!!
Success rate is 80 percent (4/5), round-trip min/avg/max = 1/3/4 ms
NOTE: The first PING packet times out due to ARP resolution. Subsequent packets will be successful.
R3#show ip interface brief
Interface IP-Address OK? Method Status Protocol
FastEthernet0/0 10.0.0.3 YES manual up up
R3#ping 10.0.0.1
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.0.0.1, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 1/3/4 ms